## Slide 1: Imported Water Opportunities
January 3, 2019
IWVGA PAC Meeting

## Slide 2: Water Balance
Baseline Model 2020 Pumping: 34,902 acre-feet per year
Baseline Model Annual Replenishment: 7,650 acre-feet per year
Year 2020 Deficit: 27,252 acre-feet per year
Basin to be brought into balance through a potential combination of conservation, recycled water, brackish water, and mainly imported water

## Slide 3: Imported Water Opportunities
AVEK Direct Use Project
LADWP Groundwater Banking/Exchange Project

## Slide 4: AVEK Direct Use Project
IWVGA purchases State Water Project Table A Entitlement (~30,000 acre-feet per year) from a current SWP contractor
Annual Table A allocation conveyed through California City pipeline, operated by Antelope Valley – East Kern Water Agency
Construction of new facilities to convey water from California City pipeline to IWVWD and Navy service areas
  28” steel pipeline
  Booster pump stations
  Storage tank

## Slide 5: LADWP Groundwater Banking/Exchange Project
IWVGA purchases State Water Project Table A Entitlement (~30,000 acre-feet per year) from a current SWP contractor
Exchange
  Provide annual Table A allocation to LADWP through MWD
  Owens Valley water provided to IWV through the Los Angeles Aqueduct
Groundwater Bank in El Paso sub basin
  LADWP stores excess Owens Valley water in IWV groundwater basin during wet years
  Stored water extracted during dry years and fed back into Los Angeles Aqueduct
  IWVGA retains a percentage of stored water for its own use
Construction of new facilities to convey water from the Los Angeles Aqueduct to IWVWD and Navy service areas
  Aqueduct turnout
  28” steel pipeline
  Spreading grounds and recovery wells
  Treatment system
  Storage tank

## Slide 6: Conceptual Costs - Summary
Capital costs
  Construction of new facilities
  Purchase of State Water Project Table A entitlement
Operations and maintenance (O&M) costs
  Facilities maintenance
  Power
Annual service costs
  State Water Project transportation fees
  Wheeling fees

## Slide 7: Conceptual Costs - Estimates
Project | Capital Costs | Annual O&M Costs | Annual Service Costs | Total Annual Cost1 | Cost per Acre-Foot2
AVEK Direct Use Project | $357,975,000 | $6,260,000 | $17,580,000 | $44,542,000 | $2,970
LADWP Groundwater Banking/Exchange Project | $235,046,000 | $2,138,000 | $12,780,000 | $28,511,000 | $1,900
Notes: 1) 30-year cost amortization at 4% interest rate 2) Annual imported water requirement of 15,000 acre-feet per year

## Slide 8: Conceptual Cost - Estimates
Project | Capital Costs | Annual O&M Costs | Annual Service Costs | Total Annual Cost1 | Cost per Acre-Foot2
AVEK Direct Use Project | $357,975,000 | $6,260,000 | $17,580,000 | $39,824,000 | $2,670
LADWP Groundwater Banking/Exchange Project | $235,046,000 | $2,138,000 | $12,780,000 | $25,413,000 | $1,700
Notes: 1) 30-year cost amortization at 2% interest rate 2) Annual imported water requirement of 15,000 acre-feet per year

## Slide 10: Health and Safety Water Requirements
Requirement: 55 gallons/capita/day (indoor domestic use only)
Equivalent to approximately 2,500 acre-feet per year for all IWV residents
Other Community Water Requirements
  Navy: 2,000 acre-feet per year
  Commercial Water Usage (gas stations, hotels, stores, etc.)
Average IWVWD Winter Usage (Dec-Feb): 40 gallons/capita/day